## Slide 1: Final Project Presentation
Group 5
Title: AES-128

## Slide 2: Introduction
Purpose: AES-128(Advanced Encryption Standard) is a symmetric encryption algorithm that encrypts and decrypts data using a fixed-length key (128 bits).
AES-128 can be used to protect the privacy of sensitive data, ensuring security during transmission and storage.

## Slide 3: Project scope
Background Introduction : It can be traced back to 1997 when finding a new advanced encryption standard to replace the then-used Data Encryption Standard (DES). DES was considered insecure due to its 56-bit key length.
What FPGA platform to implement on : KV260
Target Specification : throughput, latency or area

## Slide 4: Project scope
System block diagram

## Slide 5: Transform input bytes to state

## Slide 6: The structure of each round

## Slide 7: SubBytes
Substitute each bytes according to the lookup table.

## Slide 8: Lookup table for SubBytes

## Slide 9: ShiftRows
Shift the bytes in each row cyclically.

## Slide 10: MixColumns
Each column of the state block is mixed using a matrix multiplication operation in GF(2^8).

## Slide 11: AddRoundKey
The round key for the current round is combined with the state block using bitwise XOR.

## Slide 12: Key Expansion
Round key 0
Round key 1
Round key 2
Round key 10

## Slide 13: Complete AES-128 Encryption process

## Slide 14: Project scope
Only support AES-128 ECB mode
Operation flow
  Program cipher key
  Stream in plaintext / Stream out ciphertext

## Slide 15: HLS work
This is the encryption part. The key is generated by GenRoundKey. You can see that a state array is first declared to store the plaintext, and then the array is subjected to a series of operations such as SubBytes, ShiftRows, MixColumns, and AddRoundKey with keys. After repeating 10 times, the ciphertext is obtained.

## Slide 16: ShiftRows:
The nth column of array shifts n bytes.

## Slide 17: MixColumns:
Here we use the Galois Field table we provide to do mixcolumns.

## Slide 18: AddRoundKey:
Here we use key and state to calculate the new state.

## Slide 19: GenRoundKey:
Here is key expansion. Use this function to generate the 10 keys we need.

## Slide 20: Sbox table:

## Slide 21: Galois field table:

## Slide 22: CMDS table:

## Slide 23: Micro-architecture exploration
Original design

## Slide 24: Micro-architecture exploration
v2

## Slide 25: Catapult HLS Result
Original design
v2

## Slide 26: Problems we’ve encountered
Catapult GUI crashes quite often
Pipeline?

## Slide 27: SCVerify

## Slide 28: Integrating into FSIC
The input and output of our aes128_en is 128-bit, but the width of axi-stream in FSIC is only 32-bit. Therefore, a control logic is added to deal with the problem.

## Slide 29: Control register map

## Slide 30: Simulation result

## Slide 31: USER DMA
Because our application accelerator is big endian, but the rest of the system is little endian. We added a register in user dma to control the conversion.

## Slide 32: FPGA Simulation
Successfully passed. All output data are correct.

## Slide 33: FPGA Emulation
Successfully passed
and no pynq board was killed by us😁

## Slide 34: Synthesis

## Slide 35: Synthesis problem
We mentioned earlier that we use a lookup table, but the synthesized circuit seems to have no ROM. It is speculated that we need additional settings during synthesis.

## Slide 36: Floorplan

## Slide 37: Error
floorplan:
An error occurred when executing the power plan. From the previous i2c_master_top.v of lab3, we learned that the input of this file includes vdd and gnd. And our own design does not have vdd, gnd.
It is speculated that i2c_master_top is a small circuit and may not need a power ring, so it directly provides vdd and gnd to the circuit.

## Slide 38: Reference
NIST FIPS 197 Advanced Encryption Standard (AES) https://csrc.nist.gov/pubs/fips/197/final
Cryptographic Standards and Guidelines - AES Development https://csrc.nist.gov/projects/cryptographic-standards-and-guidelines/archived-crypto-projects/aes-development
GitHub link of our work: https://github.com/ruei7916/ASoC-Final-Project