## Slide 1
Optical Flow Accelerator
Group 6
111061545 陳揚哲、112501538 葉承泓
Final Project:
(*註: This powerpoint slide template is from Slidesgo.)

## Slide 2
Table of contents
Block Diagram
Data flow & control flow
Hardware Matmul
FIR throughput
01
02
03
04
Firmware latency
Insights
05
06
07
Synthesis report
Latency calculating in testbench
Measurement of QOS

## Slide 3
FIR (with hardware & DMA & SDRAM)：
  總共 3058 個clock cycles
  Compare to lab4-2：FIR with software：1510415個clock cycles
  Compare to lab4-2：FIR with hardware：551675個clock cycles
MM (hardware accelerator)
  總共 195 個clock cycles
  ideally：48個clock cycles
  Compare to lab6：MM with software：203852個clock cycles
Qsort (firmware)
  總共 8305 個clock cycles
  Compare to lab6： Qsort with software (without improvement techniques)：97082個clock cycles
Latency performance

## Slide 4
https://github.com/cornell-zhang/rosetta/tree/master/optical-flow
Final project –– optical flow accelerator

## Slide 5
Brief background introduction
HLS implementation (lab2)
  HLS code
  algorithm C v.s. HLS simulation
  HLS synthesis
FSIC simulation (lab1)
  Integrate into FSIC
  FSIC simulation
FSIC-FPGA (lab4)
  FSIC-FPGA simulation
  FSIC-FPGA validation (onlineFPGA)
Performance comparison
Outline

## Slide 6
Introduction
01

## Slide 7
Block Diagram
01

## Slide 8
Problem statement:
  Context: The target application is “optical flow” used in image signal processing (ISP).
  Issue:
  Objective:
Brief background introduction
The problem for optical flow computation is usually its computational complexity. Therefore it often needs large latency with software, and hard to implement in real time.
We would like to improve the computational latency and throughput of optical flow, in order to implement it in real time.

## Slide 9: Optical-flow algorithm
Optical flow is used to estimate the motion of an object by comparing the differences in light intensities between two consecutive frames.
General assumptions: “brightness constancy equation”
  The pixel intensities of an object do not change between consecutive frames.
  Take Taylor series expansion with respect to on the right-hand side of the above equation, assuming x(t), y(t) are functions of :
  where is Taylor remainder.

## Slide 10
Brief background introduction

## Slide 11
Brief background introduction

## Slide 12
Brief background introduction

## Slide 13
Brief background introduction

## Slide 14
Brief background introduction

## Slide 15
Brief background introduction

## Slide 16
Brief background introduction

## Slide 17
Brief background introduction

## Slide 18
Project Scope:
  Background Introduction:
Final project proposal –– optical flow accelerator

## Slide 19
LK method derivation:
Brief background introduction
A
C
D
B
F
E

## Slide 20
gradient_xy_calc
gradient_z_calc
gradient_weight_y
gradient_weight_x
outer_product
tensor_weight_y
tensor_weight_x
flow_calc
gradient_xy_calc
gradient_t_calc
Frame 1
Frame 0
Frame 2
Frame 3
Frame 4
gradient_x
gradient_y
gradient_t
gradient_xy_calc
gradient_t_calc
gradient_weight_y
gradient_weight_x
outer_product
tensor_weight_y
tensor_weight_x
flow_calc
gradient_weight_y
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs

## Slide 21
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y

## Slide 22
Software / algorithm C (reference code):
  System block diagram, with its operation flow:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y

## Slide 23
Software / algorithm C (reference code):
  1. gradient_xy_calc:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x (Ix)
gradient_y (Iy)
Frame 2

## Slide 24
Software / algorithm C (reference code):
  1. gradient_xy_calc:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x (Ix)
gradient_y (Iy)
Frame 2

## Slide 25
Frame 0
Frame 1
Software / algorithm C (reference code):
  2. gradient_t_calc:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
Frame 2
Frame 3
Frame 4
gradient_t (It)

## Slide 26
Software / algorithm C (reference code):
  3. gradient_weight_y:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
out
gradient_x / gradient_y / gradient_t
gradient_weight_y

## Slide 27
Software / algorithm C (reference code):
  4. gradient_weight_x:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
y_filtered.x / y_filtered.y / y_filtered.z
 |  |  | out |  |  | 

## Slide 28
Software / algorithm C (reference code):
  4. gradient_weight_x:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
y_filtered.x / y_filtered.y / y_filtered.t
 |  |  | out |  |  | 
gradient_weight_x

## Slide 29
Software / algorithm C (reference code):
  5. outer_product:
    For every pixel, compute:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y

## Slide 30
out
 | out | 
gradient_x (Ix)

## Slide 31
Software / algorithm C (reference code):
  5. outer_product:
    For every pixel, compute:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
filtered_gradient.x
filtered_gradient.y
filtered_gradient.t
out_product[0]
out_product[1]
out_product[2]
out_product[3]
out_product[4]
out_product[5]

## Slide 32
Software / algorithm C (reference code):
  6. tensor_weight_y:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
filtered_gradient.x
filtered_gradient.y
filtered_gradient.z
tensor_weight_y
out_product[0]
out_product[1]
out_product[2]
out_product[3]
out_product[4]
out_product[5]

## Slide 33
Software / algorithm C (reference code):
  7. tensor_weight_x:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
filtered_gradient.x
filtered_gradient.y
filtered_gradient.t
tensor_weight_x
tensor_y[0]
tensor_y[1]
tensor_y[2]
tensor_y[3]
tensor_y[4]
tensor_y[5]

## Slide 34
Software / algorithm C (reference code):
  8. flow_calc:
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
filtered_gradient.x
filtered_gradient.y
filtered_gradient.t
outputs
tensor[0]
tensor[1]
tensor[2]
tensor[3]
tensor[4]
tensor[5]

## Slide 35
HLS implementation
02
(lab 2)

## Slide 36
Software / algorithm C (reference code):
Reference software
gradient_xy_calc
gradient_t_calc
2
Frame 0
1
3
4
gradient_x
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_xy_calc

## Slide 37
HLS data flow:
HLS implementation
gradient_t_calc
2
Frame 0
1
3
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
4
Input channel:
8 bits 5 = 40 bits
 not allowed for FSIC design (32 bit)
Input channel:
8 bits 4 = 32 bits
 fit FSIC design (32 bit)

## Slide 38
HLS data flow:
HLS implementation
gradient_t_calc
2
Frame 0
1
3
4
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
  Input channel can have only ONE receiver

## Slide 39
HLS data flow:
  Input channel can have only ONE receiver
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
gradient_x (Ix)
Frame 2
gradient_y (Iy)
Frame 2
Frame 0
Frame 1
Frame 2
Frame 3
Frame 4
gradient_t (It)
We can get It right now
We can get Ix after 2-pixel
We can get Iy after 2-row
If first compute It  we need 2*row FIFO depth  Catapult can only support up to 128 FIFO depth
If first compute Ix  we need (2*row-2) FIFO depth  Catapult only support up to 128 FIFO depth

## Slide 40
HLS data flow:
HLS implementation
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
  Input channel can have only ONE receiver

## Slide 41
HLS data flow:
HLS implementation
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
  Input channel can have only ONE receiver
Past frame 3
Past
frame 0~3
 Iy (gradient_y_calc) first, then parallelize Ix and It

## Slide 42
HLS inplementation –– algorithm C

## Slide 43
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  1-1. gradient_y_calc:
sign bit +「個位數字」
gradient_y (Iy)
Frame 2
Line buffer 2x
Line buffer 2x
Line buffer 8x
Line buffer 8x
in
Input type:
Output type:
Buffer type:
frames_t (ac_int<32, false>)
pixel_t (ac_fixed <32,13, true, AC_RND, AC_WRAP>)
input_t (ac_fixed<8, 8, false, AC_RND, AC_WRAP>)
frames_t (ac_int<32, false>)
input2x_t (ac_int<16>)
input8x_t (ac_int<64>)
Line buffer 8x
out
Line buffer 2x

## Slide 44
HLS implementation –– HLS code
gradient_x (Ix)
Frame 2
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  1-2. gradient_x_calc:
pixel buffer
in
out
sign bit +「個位數字」
Input type: input_t (ac_fixed<8, 8, false, AC_RND, AC_WRAP>)
Output type: pixel_t (ac_fixed <32,13, true, AC_RND, AC_WRAP>)

## Slide 45
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  2. gradient_t_calc:
Frame 1
Frame 2
Frame 3
Frame 4
gradient_t (It)
in
out
Input type:
Output type:
frames_t (ac_int<32, false>)
pixel_t (ac_fixed<32,13, true, AC_RND, AC_WRAP>)

## Slide 46
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  3. gradient_weight_y:
Input type:
Output type:
Buffer type:
pixel_t (ac_fixed<32,13, true, AC_RND, AC_WRAP>)
pixel_t (ac_fixed<32,13, true, AC_RND, AC_WRAP>)
pixel_t (ac_fixed<32,13, true, AC_RND, AC_WRAP>)
pixel_t[3] (ac_fixed<32,13, true, AC_RND, AC_WRAP>[3])
pixel2x_t (ac_int<64>)
out
gradient_x / gradient_y / gradient_t
gradient_weight_y
Line buffer x/y/t
Line buffer x/y/t
Line buffer x/y/t
Line buffer x/y/t
Line buffer x/y/t
in
Line buffer x/y/t
Line buffer x/y/t
out
unsigned  no sign bit

## Slide 47
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19
18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 | 55 | 54 | 53 | 52 | 51
50 | 49 | 48 | 47 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34 | 33 | 32
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19
18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  3. gradient_weight_y:
    How to store pixel values to line buffers? Because ac_fix<> type does NOT support .set_slc() and .slc<>() method, we change them into ac_int type bit-by-bit:
Buffer type:
pixel2x_t (ac_int<64>)
Input type:
pixel_t (ac_fixed<32,13, true, AC_RND, AC_WRAP>)
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19
18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 48
tensor_y
tensor
outputs
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_weight_x
flow_calc
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  4. gradient_weight_x:
Input type:
Output type:
pixel_t[3] (ac_fixed<32,13, true, AC_RND, AC_WRAP>[3])
pixel_t[3] (ac_fixed<32,13, true, AC_RND, AC_WRAP>[3])
y_filtered.x / y_filtered.y / y_filtered.t
 |  |  | out |  |  | 
gradient_weight_x
pixel buffer
in
out

## Slide 49
Line buffer [6]
Line buffer [6]
Line buffer [6]
pixel buffer

## Slide 50
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  5. outer_product:
filtered_gradient.x
filtered_gradient.y
filtered_gradient.t
out_product[0]
out_product[1]
out_product[2]
out_product[3]
out_product[4]
Input type:
Output type:
pixel_t[3] (ac_fixed<32,13, true, AC_RND, AC_WRAP>[3])
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
out_product[5]

## Slide 51
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  6. tensor_weight_y:
Input type:
Output type:
Buffer type:
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
outer2x_t (ac_int<64*12>)
filtered_gradient.x
filtered_gradient.y
filtered_gradient.z
out_product[0]
out_product[1]
out_product[2]
out_product[3]
out_product[4]
out_product[5]
tensor_weight_y
out
in

## Slide 52
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  6. tensor_weight_y:
unsigned  no sign bit
Input type:
Output type:
Buffer type:
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
outer2x_t (ac_int<64*12>)

## Slide 53
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  7. tensor_weight_x:
Input type:
Output type:
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
filtered_gradient.x
filtered_gradient.y
filtered_gradient.z
out_product[0]
out_product[1]
out_product[2]
out_product[3]
out_product[4]
out_product[5]
tensor_weight_x
in
out
shift

## Slide 54
out_product[0]
out_product[1]
out_product[2]
out_product[3]
out_product[4]
out_product[5]
tensor_weight_x
in
out

## Slide 55
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate:
Input type:
Output type:
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
shift
tensor_value.val[0] = tensor0.val[0]*TENSOR_FILTER[0] + tensor1.val[0]*TENSOR_FILTER[1] + tensor2.val[0]*TENSOR_FILTER[2];
tensor_value.val[1] = tensor0.val[1]*TENSOR_FILTER[0] + tensor1.val[1]*TENSOR_FILTER[1] + tensor2.val[1]*TENSOR_FILTER[2];
tensor_value.val[2] = tensor0.val[2]*TENSOR_FILTER[0] + tensor1.val[2]*TENSOR_FILTER[1] + tensor2.val[2]*TENSOR_FILTER[2];
tensor_value.val[3] = tensor0.val[3]*TENSOR_FILTER[0] + tensor1.val[3]*TENSOR_FILTER[1] + tensor2.val[3]*TENSOR_FILTER[2];
tensor_value.val[4] = tensor0.val[4]*TENSOR_FILTER[0] + tensor1.val[4]*TENSOR_FILTER[1] + tensor2.val[4]*TENSOR_FILTER[2];
tensor_value.val[5] = tensor0.val[5]*TENSOR_FILTER[0] + tensor1.val[5]*TENSOR_FILTER[1] + tensor2.val[5]*TENSOR_FILTER[2];
32 bit | 32 bit
1 bit | 31 bit
32 bit | 32 bit
1 bit | 31 bit
32 bit | 32 bit
1 bit | 31 bit
ac_fixed<64,32>
ac_fixed<32,1>
32 bit | 32 bit | 32 bit
tensor_long_pixel_t
ac_fixed<64+32,32>

## Slide 56
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
Input type:
Output type:
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
32 bit | 32 bit | 32 bit
32 bit | 32 bit | 32 bit
32 bit | 32 bit | 32 bit
32 bit | 32 bit | 32 bit
32 bit | 32 bit | 32 bit
32 bit | 32 bit | 32 bit

## Slide 57
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
Input type:
Output type:
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit

## Slide 58
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 32 bit | 32 bit
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 32 bit | 32 bit
not
used
not
used
Does NOT provide any useful information
The value is so small that LSB is also important
sign bit

## Slide 59
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 32 bit | 32 bit
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 32 bit | 32 bit
not
used
not
used
We want to remove common part
(multiply them by the same number)
sign bit
Try to find the leftmost bit that is different to the sign bit

## Slide 60
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
not
used
sign bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Method 1: shift one by one
0
0
0
1
0
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
All the same as sign bit.
not
used

## Slide 61
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
not
used
sign bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Method 1: shift one by one
0
0
0
1
0
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
All the same as sign bit.
not
used

## Slide 62
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
not
used
sign bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Method 1: shift one by one
0
0
0
1
0
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
All the same as sign bit.
not
used

## Slide 63
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
not
used
sign bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Method 1: shift one by one
0
0
0
1
0
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
All the same as sign bit.
not
used

## Slide 64
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
not
used
sign bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Method 1: shift one by one
0
0
0
1
0
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
Not all the same as sign bit.
not
used
Output the MSB 32 bits

## Slide 65
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
not
used
sign bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Method 1: shift one by one
 Problem: need “while” loop, which cannot be unrolled because of unbounded  Bad performance.
0
0
0
1
0
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
not
used

## Slide 66
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 32 bit | 32 bit
not
used
sign bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
Method 2: use hardware logic gates
0
0
0
1
0
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
not
used
We try to find the leftmost bit that is different to the sign bit

## Slide 67
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
shift
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
shift
tensor_value.val[0]
tensor_value.val[1]
tensor_value.val[2]
tensor_value.val[3]
tensor_value.val[4]
tensor_value.val[5]
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 32 bit | 32 bit
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 32 bit | 32 bit
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 32 bit | 32 bit
not
used
not
used
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 32 bit | 32 bit
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 32 bit | 32 bit
XOR with sign bit
XOR with sign bit
XOR with sign bit
XOR with sign bit
XOR with sign bit
Method 2: use hardware logic gates
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 32 bit | 32 bit
bitwise OR

## Slide 68
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
gradient_y
gradient_t
gradient_x
Method 2: use hardware logic gates
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 32 bit | 32 bit
bitwise OR
We want to find the position of the “leftmost 1”:
1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
32 bit | 32 bit
flip
~flip
Then to find the position of the “rightmost 1”:
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
32 bit | 32 bit
flip (=~flip+1)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
32 bit | 32 bit
flip & (flip)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
32 bit | 32 bit
The position of the only “1” is our goal.

## Slide 69
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  tensor_weight_x:
    To make the result more accurate, and not to waste too many bits:
gradient_y
gradient_t
gradient_x
Method 2: use hardware logic gates
We want to find the position of the “leftmost 1”:
flip & (flip)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
32 bit | 32 bit
The position of the only “1” is our goal.
 But we cannot use “while” loop to find the position; instead, we use the following technique:
flip & (flip)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
32 bit | 32 bit
0
1
2
3
4
5
6
7
………………………………………………………………….
31
 Then we can get the position without using “while” loop !!

## Slide 70
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  7. tensor_weight_x:
Input type:
Output type:
outer_pixel_t[6] (ac_fixed<64,32, true, AC_RND, AC_WRAP>[6])
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
shift

## Slide 71
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  8. flow_calc:
Input type:
Output type:
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
output_stream_t (ac_int<32>)
shift
filtered_gradient.x
filtered_gradient.y
filtered_gradient.t
outputs
tensor[0]
tensor[1]
tensor[2]
tensor[3]
tensor[4]
tensor[5]

## Slide 72
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  8. flow_calc:
shift
Because of complexity of “division” operation, we do not implement division in hardware; instead, we output “denominator”, “numerator of u”, “numerator of v” on the same output stream, by time-division method
We use the same technique to shift value for more accuracy. But the total shift value should be “shift in tensor_weight_x” 2 + “shift in flow_calc” because of square operation.
We use shift_threshold to filter out those with too small denominator, which means Ix=Iy=It=0, and output should be u=v=0.a

## Slide 73
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  8. flow_calc:
Input type:
Output type:
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
output_stream_t (ac_int<32>)
shift

## Slide 74
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  8. flow_calc:
shift
Because of complexity of “division” operation, we do not implement division in hardware; instead, we output “denominator”, “numerator of u”, “numerator of v” on the same output stream, by time-division method
Input type:
Output type:
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
output_stream_t (ac_int<32>)

## Slide 75
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  8. flow_calc:
shift
We use the same technique to shift value for more accuracy.
Input type:
Output type:
tensor_int_pixel_t[6] (ac_int<32>[6])
shift_t (ac_int<ac::nbits<(64+32)*2+(32*2)>::val,false>)
output_stream_t (ac_int<32>)

## Slide 76
HLS implementation –– HLS code
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS code:
  8. flow_calc:
shift
We use the same technique to shift value for more accuracy. But the total shift value should be “shift in tensor_weight_x” 2 + “shift in flow_calc” because of square operation.
We use shift_threshold to filter out those with too small denominator, which means Ix=Iy=It=0, and output should be u=v=0.

## Slide 77
HLS implementation –– HLS simulation

## Slide 78
HLS implementation –– HLS simulation
algorithm
HLS

## Slide 79
HLS implementation –– HLS simulation

## Slide 80
HLS implementation –– HLS simulation

## Slide 81
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
HLS Top Design :
tensor
shift

## Slide 82
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
1-1. gradient_y_calc :
  Input data along x-axis, need use line buffer
  Configuration Port is set as [direct input]
  Kernel array size = 5, so line buffer = 4
tensor
shift

## Slide 83
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
1-2. gradient_x_calc :
  Input data is from gradient_y_calc, which is along x-axis
  Configuration Port is set as [direct input]
  Kernel array size = 5
tensor
shift

## Slide 84
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
2. gradient_t_calc :
  Input data is from gradient_y_calc, which is along x-axis
  Configuration Port is set as [direct input]
  Kernel array size = 4
tensor
shift

## Slide 85
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
3. gradient_weight_y :
  Input data is along x-axis, need use line buffer
  Apply FIFO for gradient_y, gradient_x and gradient_t.
  Kernel array size = 7, need 18 line buffer
tensor
shift

## Slide 86
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
4. gradient_weight_x :
  Input data is from gradient_weight_y
  Configuration Port is set as [direct input]
  Kernel array size = 7
tensor
shift

## Slide 87
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
5. outer_product:
  Input data is from gradient_weight_x
  Configuration Port is set as [direct input]
  Output is an array, we set it as register
tensor
shift

## Slide 88
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
6. tensor_weight_y:
  Input data is an array, which is from outer_product
  Kernel array size = 3, line buffer = 2
  Input array should be stored by register for II = 1
tensor
shift

## Slide 89
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
7. tensor_weight_x:
  Input data is an array, which is from tensor_weight_y
  Input array should be stored by register for II = 1
tensor
shift

## Slide 90
HLS implementation –– HLS Synthesis
gradient_t_calc
gradient_y
gradient_t
y_filtered
gradient_weight_x
filtered_gradient
outer_product
out_product
tensor_weight_y
tensor_y
tensor_weight_x
tensor
flow_calc
outputs
gradient_weight_y
gradient_x
gradient_y_calc
gradient_x_calc
Input channel
Frame 0~3
(32 bits)
Past frame 3
Past
frame 0~3
8. flow_calc:
  Input data is an array, which is from tensor_weight_x
  Input array should be stored by register for II = 1
  Output data align in one stream out channel
  One input data generate 3 output data (II at least = 3)

## Slide 91
FSIC simulation
03
(lab 1)

## Slide 92
FSIC integration
  Check the design of HLS (I/O)
  Direct in type channel should be set as AXI-lite interface (configuration)
  Ac_channel is set as stream interface
  Assign the external SPRAM for HLS design
FSIC simulation –– Integrate into FSIC

## Slide 93
Since our design using lots of line buffer, there are 24 SPRAM interfaces.
Specify the interface of the signal.
FSIC simulation –– Check the design of HLS
AXI-lite interface
Stream interface
SRAM interface
SRAM interface

## Slide 94
reg_rst = 12’h0000_0000_0000, Width_In = 12’h0000_0000_0100
Height_In = 12’h0000_0000_0200, shift_threshold = 12’h0000_0000_0300
FSIC simulation –– AXI-lite interface
AXI-lite interface

## Slide 95
Since our design using lots of line buffer, there are 24 SPRAM interfaces.
FSIC simulation –– Stream interface
Stream interface

## Slide 96
Our 24 SRAM interface will need different depth and word size SRAM
FSIC simulation –– SRAM interface
SRAM interface
SRAM interface

## Slide 97
FSIC simulation –– FSIC simulation result

## Slide 98
FSIC-FPGA
04
(lab 4)

## Slide 99
For the origin userDMA, the depth is set as constant in header file in lab4.
  The userDMA depth should be a programable parameter.
If the data count (final_s2m_len) is equal to programmed data length (in_s2m_len)
  The userDMA done signal = 1
  Jump out of while loop to stop receiving stream output data.
FSIC-FPGA –– UserDMA

## Slide 100
FSIC-FPGA –– FSIC-FPGA simulation

## Slide 101
FSIC-FPGA –– FSIC-FPGA simulation

## Slide 102
In FSIC-FPGA validation, the process is similar to lab4.
  We need apply UserDMA to set feed input data and dump the output data
Here is the process to add userDMA
  Assign address to config userDMA
  Connect the userDMA to memory interface (for stream in/out interface)
  Connect the stream_in data for our user project
  Read the stream_out data to dump the result
FSIC-FPGA –– FSIC-FPGA validation

## Slide 103
FSIC-FPGA ––address for userDMA

## Slide 104
FSIC-FPGA –– Connect to memory interface

## Slide 105
FSIC-FPGA –– stream_in for user_project

## Slide 106
FSIC-FPGA –– stream_out dump result

## Slide 107
After generating bitstream, we upload the following items to onlineFPGA:
FSIC-FPGA –– FSIC-FPGA validation
caravel_fpga.bit
caravel_fpga.hwh
fsic.hex
caravel_fpga_fsic.ipynb
frame1.hex
frame2.hex
frame3.hex
frame4.hex

## Slide 108
The running result was:
  Choose user project 2 (OpticalFlow IP):
FSIC-FPGA –– FSIC-FPGA validation

## Slide 109
The running result was:
  Output:
FSIC-FPGA –– FSIC-FPGA validation

## Slide 110
Performance
05

## Slide 111
II = 1, flow_calc II = 3, resource not available
II = 2, flow_calc didn’t pipelined.

## Slide 112
II = 2, flow_calc II = 3 (half utilize, since the problem of pipeline)

## Slide 113
II = 3, flow_calc II = 3, stuck in FIFO

## Slide 114
II = 2, flow_calc II = 4. (Correct)

## Slide 115
Reference:
  Y. Gong et al., "A Real-Time and Efficient Optical Flow Tracking Accelerator on FPGA Platform," in IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 70, no. 12, pp. 4914-4927, Dec. 2023, doi: 10.1109/TCSI.2023.3298969.
  Open source (C code & reference HLS): https://github.com/cornell-zhang/rosetta/tree/master/optical-flow
Final project –– optical flow accelerator

## Slide 117
Project Scope:
  The area of work: improving the latency of optical flow computation
  FPGA platform to implement on: KV260
  Target Specification:
    Throughput: better than reference benchmark, Rosetta benchmark (41.2 frames/s)
    Accuracy: can use estimation to speed up the computation
    Speedup: better than Rosetta benchmark (runtime = 24.3 ms)
    Area: resource usage less than Rosetta benchmark (LUTs = 42878; FFs = 61078; BRAMs = 54; DSPs = 454)
    Proposed design methodology: using dataflow design
Final project proposal –– optical flow accelerator

## Slide 118
Thank you!

## Slide 120: Jupiter Venus Saturn 01 02 03
Jupiter is a gas giant and the biggest planet in the Solar System. It's the fourth-brightest object in the night sky. It was named after the Roman god of the skies and lightning
Venus has a beautiful name and is the second planet from the Sun. It’s terribly hot and its atmosphere is poisonous. It’s the second-brightest natural object in the night sky
Saturn is a gas giant and has several rings. It's composed mostly of hydrogen and helium. It was named after the Roman god of wealth and agriculture. It’s the sixth planet from the Sun